## Slide 1
AI-Driven Two-Tier Landslide Early Warning & Disaster Resilience Grid for North-East India (NER)
XGBoost Two-Tier Stacking | Meta-Calibrator Fusion | Real-Time IoT Telemetry | InSAR Ground Deformation | Dijkstra Evacuation Routing | OASIS CAP v1.2 Multi-Lingual Alert
Dr. R. Rajmohan | Disaster Management Research Group, SRM Institute of Science & Technology | Coord: 20-30N, 88-98E | NH-10, NH-27, NH-29, NH-44
Artificial Intelligence
Geotechnical Eng.
Satellite Remote Sensing
Disaster Risk Reduction
Study Context & Problem Statement
North-East India reports >200 monsoon fatalities annually from landslides across 8 national highways. Existing threshold systems lack spatial specificity and probabilistic calibration. MINDMELD decouples static terrain susceptibility S(x) from dynamic hydro-geotechnical triggers T(x,t) via a two-tier XGBoost stacking architecture with a meta-calibrator fusion engine, producing calibrated P_fused mapped to 4 NDMA operational alert tiers.
Bounding Box
20N-30N 88E-98E
8 NE States
Assam+7 states
Dataset
1152 events 2007-2019
IoT Nodes
40-node grid
Two-Tier XGBoost Stacking Architecture
TIER 1 - Static Susceptibility S(x)
Inputs: slope, elevation, aspect_sin, aspect_cos, curvature, dist_to_road_km XGBoost: n_est=180, max_depth=6, eta=0.30, lambda=1.0, seed=42 Output: P_susc in [0,1] | Logit: zeta_1 = ln[P/(1-P)]
TIER 2 - Dynamic Trigger T(x,t)
Inputs: rain_24h, rain_48h_prior, rain_72h, rain_7d, API_7d, r24_seasonal_anom, api_seasonal_anom XGBoost: n_est=100, max_depth=6, eta=0.30, base_score=0.26 Output: P_trig in [0,1] | Logit: zeta_2 = ln[P/(1-P)]
META-CALIBRATOR - LR Fusion Engine
Z = [zeta_1, zeta_2]^T | LR: L2 penalty, C=1.0, lbfgs P_fused = sigma(w0 + w1*zeta_1 + w2*zeta_2) | Threshold theta=0.35 R_k = f(P_fused) -> NDMA {GREEN | YELLOW | ORANGE | RED}
Geotechnical Physics - Infinite Slope Factor of Safety
Terzaghi Effective Stress
sigma_prime = (gamma_s*z - gamma_w*h_w)*cos^2(beta)
Mohr-Coulomb Shear Strength
tau_f = c_prime + sigma_prime * tan(phi_prime)
Infinite Slope FS
FS = [c_prime + (gamma_s*z - gamma_w*h_w)*cos^2(beta)*tan(phi_prime)] / [gamma_s*z*sin(beta)*cos(beta)]
Critical Rainfall Depth h_w*
h_w* = z - [c_prime/(gamma_w*cos^2(beta)*tan(phi_prime))] + [z*tan(beta)/tan(phi_prime)]
Richards PDE (Transient Seepage)
d(theta)/dt = d/dz[K(h)*(dh/dz + 1)] - S(z,t)
Antecedent Precip Index
API_t = SUM[k=0..n] P_(t-k) * exp(-k/tau) [tau=7-day decay]
Seasonal Anomaly
Anom_t = (P_t - mu_clim(doy)) / sigma_clim(doy)
TreeSHAP Global Dynamic Feature Attribution
Fig 6. Global TreeSHAP - rain_48h_prior dominates (34.70%)
Calibrated Risk to NDMA Alert Tier Mapping
Fig 7. P_fused -> R_k (1-10) -> NDMA {Green|Yellow|Orange|Red} theta=0.35
Hydro-Geotechnical Feature Correlation Matrix
Fig 8. Pearson Correlation - Static + Dynamic Feature Matrix (13 vars)
Performance Metrics Dashboard
Holdout Test | Spatial Block OOF | LOYO Temporal
Test Partition (N=52)
Accuracy
94.23%
Precision
85.71%
POD/Recall
92.31%
ROC-AUC
0.9803
PR-AUC
0.9208
Brier
0.0410
Spatial Block OOF (N=346)
Accuracy
85.84%
Precision
75.95%
POD/Recall
66.67%
ROC-AUC
0.8816
PR-AUC
0.8177
Brier
0.0991
LOYO Temporal (N=346, 2007-2019)
Accuracy
71.10%
Precision
41.67%
POD/Recall
27.78%
ROC-AUC
0.5925
PR-AUC
0.3870
Brier
0.2176
Confusion Matrix - Test Partition (theta=0.35, N=52)
Pred 0
Pred 1
Act 0
37
2
Act 1
1
12
TP=12
TN=37
FP=2
FN=1
Fig 1. Confusion Matrix Heatmap (Test N=52, theta=0.35)
Fig 2. ROC Curve (AUC=0.9803) - Two-Tier Calibrated Model
Global TreeSHAP Dynamic Feature Attribution
Trigger Model - Mean |SHAP Value| ranking
rain_48h_prior
1.8878 (34.7%)
r24_seasonal_anom
0.8781 (16.1%)
rain_24h_obs
0.7105 (13.1%)
rain_7d_prior
0.6528 (12.0%)
api_seasonal_anom
0.5773 (10.6%)
rain_72h_prior
0.4913 (9.0%)
api_7d
0.2419 (4.5%)
Precision-Recall & Calibration Reliability Curves
Fig 3. PR Curve (AUC=0.9208)
Fig 4. Reliability (Brier=0.0410)
Leave-One-Year-Out Temporal Validation (2007-2019)
Year
N
Acc%
Prec%
POD%
FAR%
AUC
2007
12
66.67
0.00
0.00
100.0
0.222
2013
4
75.00
0.00
0.00
0.00
1.000
2014
21
52.38
0.00
0.00
100.0
0.378
2016
20
75.00
0.00
0.00
0.00
0.400
2018
277
64.62
23.53
16.90
76.47
0.564
2019
12
66.67
33.33
33.33
66.67
0.296
MEAN
346
71.10
41.67
27.78
58.33
0.593
Fig 5. LOYO Multi-Year Accuracy Bar (Mean=71.10%)
Real-Time System Components
Sentinel-1A InSAR
C-Band SAR | LOS ~1-3 mm Interferogramme unwrapping
40-Node IoT Grid
Piezometers + MEMS IPI AsyncIO FastAPI @ 5-min poll
Dijkstra EV-Router
NetworkX multigraph G=(V,E,W) C_risk = 100*P^2 + 10*P + 1
CAP v1.2 Alerts
OASIS XML/JSON + Haversine 8-language SMS broadcast engine
AI-Driven Two-Tier Landslide EWS | Dr. R. Rajmohan | SRM Institute of Science & Technology
Dataset: N=1,152 events (2007-2019) | Python 3.14 + XGBoost + scikit-learn + FastAPI | 2026